## Slide 1: Quantifying the effectiveness of various air pollution reduction schemes in Delhi
Presented by:
Bharati Khanijo,
Krithika Subramanian
Sayantika Ghosh
Under the guidance of:
Professor Rajesh Sundaresan
Professor Ramesh Hariharan

## Slide 2
Objective:
To analyze the concentration of various pollutants measured by different measuring stations in Delhi and estimate the effectiveness of different measures taken by the government to improve air quality in the city

## Slide 3
Motivation

## Slide 4
DELHI AIR POLLUTION
Most polluted capital in the world
Huge health impact
Effectiveness of the policy ???

## Slide 5: Sources of Air Pollution in Delhi
https://www.downtoearth.org.in/news/air/delhi-air-pollution-identifying-perpetrators-and-fixing-responsibility-56240

## Slide 6: Effects on Health
Short-term effects
  Irritation to the eyes, nose and throat
  Respiratory infections such as bronchitis
  Pneumonia
  Headaches
  Nausea
  Allergic reactions.
  Short-term air pollution can aggravate the medical conditions of individuals with asthma and emphysema

## Slide 7: Effects on Health
Long-term Effects
  Chronic respiratory diseases
  Lung cancer
  Heart disease
  Damage to the brain, nerves, liver, or kidneys.
  Continual exposure to air pollution affects the lungs of growing children and may aggravate or complicate medical conditions in the elderly.
  Pre-mature Deaths

## Slide 8
AQI | Color Code | Possible Health Impacts
0-50 | Good | minimal impact
51-100 | Satisfactory | minor breathing discomfort to sensitive people
101-200 | Moderate | breathing discomfort to the people with lung disease such as asthma and discomfort to people with heart disease, children and older adults
201-300 | Poor | breathing discomfort to people on prolonged exposure and discomfort to people with heart disease with short exposure
301-400 | Very Poor | respiratory illness to the people on prolonged exposure. Effect may be more pronounced in people with lung and heart diseases
401-500 | Severe | respiratory effects even on healthy people and serious health impacts on people with lung/heart diseases
Above 500 | Emergency | Emergency

## Slide 9
Anand Vihar, Delhi

## Slide 10
Mandir Marg, Delhi

## Slide 11: Our Approach

## Slide 12
Problem Domain Selection
Problem Selection
Data Collection
Understanding Data
Missing Values
Diurnal and Seasonal Variation
Correlation
Predicting Pollutant Concentration
Comparing Actual Pollutant Concentration with Predicted Pollutant Concentration
Summarizing Analysis

## Slide 13
Calculating Correlation

## Slide 14: Pearson's correlation coefficient
For Anand Vihar Measuring Station

## Slide 15
Predicting Pollutant Concentration

## Slide 16: Predicting Pollutant Concentration (Basic Idea)
Concentration Predictor
Average Temperature in °C
Barometric Pressure in mmHg
Relative Humidity %
Solar Radiation in W/m2
Wind Speed in m/s
Day of the year
Minute of the day
Previous known Concentration of Given Pollutant
Predicted concentration of
given Pollutant

## Slide 17: Predicting Pollutant Concentration (Continued)
Concentration Predictor
(Polynomial of degree 2)
Average Temperature in °C
Barometric Pressure in mmHg
Relative Humidity %
Solar Radiation in W/m2
Wind Speed in m/s
Day of the year
Minute of the day
Previous known Concentration of Given Pollutant
Predicted concentration of
given Pollutant

## Slide 18
Comparing
Actual Pollutant Concentration
with the
Predicted Pollutant Concentration

## Slide 19: Schemes analysed
Schemes | Implemented Date
Odd Even rational Scheme | 2019 – Nov 4 to 15 2017 – Nov 13 to 17 2016 – Jan 1 to 15 and April 15 to 30
Banning of construction | 2016 – Nov 9 to 15 2019 – Nov 12 to 23
Combination of banning construction Activity and banning entry of diesel trucks more than 10years | 2017 – Nov 8 to 14
Banning construction activities and Dirty fuel based Industries | 2018 – Dec 24 to 26
Banning construction activities, Dirty fuel based Industries and entry of Trucks | 2018 – Nov 8 to 12

## Slide 20: Effect of Odd Even rational Scheme on NO2
Mandir Marg
Anand Vihar

## Slide 21: Effect of banning of construction on PM10
Mandir Marg
Anand Vihar

## Slide 22: Improvement in Anand Vihar Station
Policy | Pollutant | Mean Concentration Reduction (microgram/m3)
Banning Construction Activities | PM 10 | 85.83
Banning Construction Activities and Entry of diesel trucks more than 10 years old | PM 10 | 5.585
 | PM 2.5 | 6.16
 | NO2 | 8.74
 | SO2 | 1.77
Banning Construction Activities and Dirty Fuel Based Industries | PM 10 | 80.76
 | PM 2.5 | 9.62
 | SO2 | 1.12
Banning Construction Activities, Dirty Fuel Based Industries and Entry of Trucks | PM 10 | 510.80
 | PM 2.5 | 325.10
 | SO2 | 3.83
* According to our pollutant prediction curves

## Slide 23: Detailed Analysis

## Slide 24: Pearson's correlation coefficient
RK Puram
Mandir Marg
Anand Vihar
Punjabi Bagh

## Slide 25: Detailed Predicted Concentration and Actual Concentration Comparitive Analysis

## Slide 26: Effect of Odd Even rational Scheme on PM10
Mandir Marg
Anand Vihar

## Slide 27: Effect of Odd Even rational Scheme on PM2.5
Mandir Marg
Anand Vihar

## Slide 28: Effect of Odd Even rational Scheme on NO2
Mandir Marg
Anand Vihar

## Slide 29: Effect of Odd Even rational Scheme on SO2
Mandir Marg
Anand Vihar

## Slide 30: Effect of banning of construction on PM10
Mandir Marg
Anand Vihar

## Slide 31: Effect of banning of construction on PM2.5
Mandir Marg
Anand Vihar

## Slide 32: Effect of banning of construction on NO2
Mandir Marg
Anand Vihar

## Slide 33: Effect of banning of construction on SO2
Mandir Marg
Anand Vihar

## Slide 34: Effect of combination of banning construction Activity and banning entry of diesel trucks more than 10years on PM10
Mandir Marg
Anand Vihar

## Slide 35: Effect of combination of banning construction Activity and banning entry of diesel trucks more than 10years on PM2.5
Mandir Marg
Anand Vihar

## Slide 36: Effect of combination of banning construction Activity and banning entry of diesel trucks more than 10years on NO2
Mandir Marg
Anand Vihar

## Slide 37: Effect of combination of banning construction Activity and banning entry of diesel trucks more than 10years on SO2
Mandir Marg
Anand Vihar

## Slide 38: Effects on banning construction activities and Dirty fuel based Industries on PM10
Mandir Marg
Anand Vihar

## Slide 39: Effects on banning construction activities and Dirty fuel based Industries on PM2.5
Mandir Marg
Anand Vihar

## Slide 40: Effects on banning construction activities and Dirty fuel based Industries on NO2
Mandir Marg
Anand Vihar

## Slide 41: Effects on banning construction activities and Dirty fuel based Industries on SO2
Mandir Marg
Anand Vihar

## Slide 42: Effects on banning construction activities, Dirty fuel based Industries and entry of Trucks on PM10
Mandir Marg
Anand Vihar

## Slide 43: Effects on banning construction activities, Dirty fuel based Industries and entry of Trucks on PM2.5
Mandir Marg
Anand Vihar

## Slide 44: Effects on banning construction activities, Dirty fuel based Industries and entry of Trucks on NO2
Mandir Marg
Anand Vihar

## Slide 45: Effects on banning construction activities, Dirty fuel based Industries and entry of Trucks on SO2
Mandir Marg
Anand Vihar

## Slide 46: Improvement in Anand Vihar Station
Policy | Pollutant | Mean Concentration Reduction (microgram/m3)
Banning Construction Activities | PM 10 | 85.83
Banning Construction Activities and Entry of diesel trucks more than 10 years old | PM 10 | 5.585
 | PM 2.5 | 6.16
 | NO2 | 8.74
 | SO2 | 1.77
Banning Construction Activities and Dirty Fuel Based Industries | PM 10 | 80.76
 | PM 2.5 | 9.62
 | SO2 | 1.12
Banning Construction Activities, Dirty Fuel Based Industries and Entry of Trucks | PM 10 | 510.80
 | PM 2.5 | 325.10
 | SO2 | 3.83
* According to our pollutant prediction curves

## Slide 47: Key Takeaways
One of the major takeaways from this study is that the concentration of pollutant decreases only in regions where that pollutant is the major contributor
Also the effect of stubble burning on our data and the implementation of various measures

## Slide 48: References
Central Pollution Control Board (CPCB) Air Quality Data, ”https://app.cpcbccr.com/ccr//caaqm-dashboard-all/caaqm-landing”
https://economictimes.indiatimes.com/news/politics-and-nation/ban-on-night-time-construction-in-ncr-extended-till-saturday/articleshow/71838547.cms
https://www.indiatoday.in/india/story/delhi-ncr-s-dirty-fuel-driven-industries-to-remain-shut-till-nov-8-epca-1615732-2019-11-05
https://www.indiatoday.in/india/story/air-pollution-sc-bans-construction-demolition-burning-of-waste-in-delhi-ncr-1615731-2019-11-05
https://economictimes.indiatimes.com/news/politics-and-nation/epca-shuts-industries-in-delhis-pollution-hotspots-bans-construction-activities-till-wednesday/articleshow/67230110.cms?from=mdr
https://www.livemint.com/Politics/MHVjYfmyoaZVnnYKg2mFzK/Delhi-air-pollution-NGT-imposes-ban-on-industrial-construc.html
https://economictimes.indiatimes.com/news/politics-and-nation/ngt-gets-cracking-on-pollution-in-delhi-ncr-bans-all-construction-work-for-7-days/articleshow/55311680.cms?from=mdr
https://www.jagranjosh.com/current-affairs/what-is-oddeven-rule-that-will-be-implemented-in-delhi-from-4-to-15-november-1568360599-1

## Slide 49: Thank You !

## Slide 52: Motivation
Delhi – the most polluted capital in the world
Given the huge impact on the health and environment Delhi Government implemented many policies to reduce the pollution levels in Delhi
The effectiveness of these policies are not still fully described.
So the main motivation behind this study is to show the quantitative effectiveness of odd even road rationing scheme over other implemented schemes.

## Slide 53: Results

## Slide 54: Challenges
In the first phase of data collection, we were having issues in downloading data from CPCB website due to slow and 404 response from server.
In the second phase of understanding the data we found that for a given station, different parts of data was missing for long continuous intervals of time due to malfunctioning of the measuring sensor.
During implementation we found that the dates of implementation of various schemes were mostly in the month of November, thus reducing the data base during that period.
Also, it was observed that several meteorological parameters have correlation with the concentration of pollutants
A major challenge we faced was to provide an estimate quantifying the benefits offered by various schemes, in the backdrop of the effect of wind, diurnal variations and other seasonal factors.

## Slide 55
Missing Data ?
Drop Corresponding Rows
No data during implementation of schemes
Simple Interpolation
Different Meteorological Parameters show different trends based on the time of the day